## Slide 1: Automatic Fastener Script
larry.pearce@mscsoftware.com

## Slide 2: This script is Perfect!
NO! NOT! NADA! m Hai! Ne! Nee! Non! Nein! Nahi! Lie! Nao! Net! Nej! Hayzr! And so on …
If you have problems or issues executing this script, I will be happy to help debug and correct …
Or, if you make additions or corrections to the script, please share with me 
~
~

## Slide 3: Features
Automatically creates flexible fasteners between holes in 2D surfaces
  Automatically finds 2D hole features
  Fastener diameter is based on the hole diameter
  Mating hole diameters must be the same within a tolerance
  Optionally creates multi-Part fasteners, i.e., between more than 2 Parts
    Note that the fastener is not continuous between the Parts. I may be able to correct this soon.
  Optionally allows mating holes to be misaligned, i.e., imperfect CAD geometry
  Hole connections can be rigid (RBE2) or compliant (RBE3)
Due to limitations in Hawk (or perhaps the programmer), the script does not currently support point-to-point connections

## Slide 4: Optional script edits (see more on next slide)
maxDia no longer used

## Slide 5: Optional script edits - details
For different unit systems or even model dimensions (big vs small), you may need to adjust the tolerance
  0.05 seems to work well for inches and mm
allowMultiUseHoles
  Set to True if you want to connect Part-to-Part-to-Part-to-<more here>
  Note that the connections are not continuous between the Parts. I hope to address this soon.
allowMisalignedHoles
  Set to False if the hole axes must be aligned within the tolerance value
keepPoints
  Currently the code creates a Point at the center of each hole (I hope to not need to do this in the future)
  Set to True if you want to keep these Points
maxDia
  Do not create a fastener if the hole diameter is greater than this. Perhaps, I should also add a minimum diameter as well
_distributionType
  Set to “compliant” or “rigid”
You can also edit the material to be used by the fasteners

## Slide 6: Script output
To the Apex script modal output form
To a log file
  Will be in the user’s temporary folder
    If unable to resolve temporary folder it will be in C:\
    If unable to write to temporary folder or C:\ it will not be output at all
  Filename will be:
    <Apex Model>_autoCreateFasteners.log

## Slide 7: Limitation
Holes must have only 1 edge
I hope to remove this limitation soon
Ok!
Ok!
NOT Ok!

## Slide 8: MountAssembly_wMidsurfaces.X_T

## Slide 9: Crew Module with ms-2.X_T

## Slide 10: Crew Module-Whole.X_T
Connecting 3 Parts

## Slide 11: Connections between more than 2 Parts
Unexploded view
Exploded view
Duplicate nodes and RBEs
I hope to be able to create a continuous fastener soon

## Slide 12: misAlignedHoles.X_T
If allowMisalignedHoles = False, the fasteners are not created

## Slide 13: Coming Attractions …
Point-to-point connections
  Requires ability to get nodes close to seed points
  May require ability to macro record seed point creation
Continuous fastener multi-Part connections
  I may be able to do this in Hawk. Stay tuned …
CBUSH connections that support Huth or other fastener stiffness calculations
  I may be able to do this in Hawk. Stay tuned …
Support for holes with more than 1 edge
  With imagination, I may be able to do this in Hawk. Stay tuned …
  If we could get geometry associated to a feature this would be easy